Limited Sportsman/Sport Series/Super Street Open Rules

- Stock type Chassis/ No tube type chassis allowed (may have tubing in front of radiator and behind rear axle).  Stock floor pan in stock location must be retained.

- Shocks must be mounted in stock location.  No heim end or coil over type shocks permitted.  No external adjustable shocks permitted.

- Wheels: 7” or 8” wheels.  Maximum 2” wheel offset.

- Tires: American Racer 7” or 8” 704, 705, or 706 series only.  No tire softening permitted!

- Spoiler: 6” High by 60” wide maximum.  Maximum height measured from ground surface shall be 40”, measured at highest point.  One spoiler per car mounted at rear of the deck lid or tail section.  No roof vanes or roof spoilers permitted.

- Carburetion: Stock factory 2-barrel carburetor or Holley 4412 2 barrel permitted.  Holley must be stock with removal or choke plate and must pass tech tool.

- Factory cast Iron intake or Edelbrock aluminum 2101 or 2116 only.  Maximum 1” carburetor adapter/spacer allowed.

- Flat top pistons only.

- Weight: 2900lbs.  With driver before race.  56% left side.

- Rear end: Factory type only.  NO quick change rears permitted.

- Steel body only.  Aftermarket nose and tails permitted.  No extended tails permitted!

- Minimum 3” ground clearance.

- 4 wheel working brakes mandatory.

- Added weight bust securely fastened and painted white.

- Full windshield required.

- Normal standard safety rules apply.

These rules are intended for fair and equitable competition.  This race is designed for the division of cars listed at the heading.  Management has the right to deem any car not within the rightful division.

White Mountain Motorsports Park weekly Street stock competitors are allowed to compete using their existing shock rule in accordance with their weekly rules. These cars will be required to weigh 2950 lbs. All other rules posted for this event apply as stated. This exeption is for weekly competitors at WMMP only.